### Textbox
Timer is a special component that is invisible. It fires one or more org.zkoss.zk.ui.event.Event after a specified delay.

Notice that the timer won't fire any event until it is attached to a page.

<label id="now"/>
<timer id="timer" delay="1000" repeats="true"
onTimer="now.setValue(new Date().toString())"/>
#### Class Name
org.zkoss.zul.Timer
#### Supported Child Components
*NONE
#### Supported Events
Event Name	Event Type
onTimer	org.zkoss.zk.ui.event.Event / Description: / Denotes the timer you specified has triggered an event. To know which timer, invoke the getTarget method in the Event class.

#### Properties
Property	Description	Data Type	Default Value
delay	Sets the delay, the number of milliseconds between successive action events. / Note : 0 means immediately	int	0
repeats	Sets whether the timer shall send Event repeatedly. / Values : true|false	boolean	false
running	Start or stops the timer. / Values : true|false	boolean	true

#### Methods
Name	Description	Data Type	Values
start	Starts the timer.	void
stop	Stops the timer.	void

#### Inherited From
Inherited From
org.zkoss.zul.imp.XulElement
org.zkoss.zk.ui.HtmlBasedComponent
org.zkoss.zk.ui.AbstractComponent